## Slide 1
Hybrid NPU + GPU Execution
Faster prompt response and lower power for on-device LLMs
Use each processor for the phase it is good at — the NPU for reading the prompt, the GPU for writing the answer — inside one unchanged application.
TARGET
Ryzen AI · Strix-class APU
FIRST MODELS
Llama-3.2-1B, then Llama-3.1-8B
ACCEPTANCE
Accuracy, not a throughput number
Design review complete · Phase 0 in progress

## Slide 2
THE OPPORTUNITY
Two phases, opposite needs
Generating text has two stages that stress hardware in completely different ways. Today we run both on the GPU, so one of them is always on the wrong processor.
READING THE PROMPT
Happens once. Processes every word at the same time.
Limited by raw compute
Best on the NPU
WRITING THE ANSWER
Repeats for every word produced. One word at a time.
Limited by memory speed
Best on the GPU
Splitting them improves how fast the first word appears, and frees each processor to idle while the other works.
Hybrid NPU + GPU Execution · MorphiZen HIP EP
2

## Slide 3
THE APPROACH
One session, two processors
The application is unchanged. Work is routed per request inside our execution provider.
Prompt
NPU
Reads the whole prompt
Runs once per request
Shared memory
handoff point
GPU
Writes the answer
Loops per word
The handoff is the shared memory itself. Nothing is transferred, converted or reorganised when work moves between processors.
No application change
Same model file, same interface, one session.
Decided per request
A conversation can switch back and forth freely.
GPU path untouched
Today's behaviour is preserved exactly.
Hybrid NPU + GPU Execution · MorphiZen HIP EP
3

## Slide 4
THE ENABLER
Why this is possible on this hardware
On these processors the NPU, GPU and CPU share the same physical memory. That is what makes the split worth doing at all.
ON A SEPARATE GRAPHICS CARD
Each processor owns its own memory.
Handing work over means copying the data across.
The copy costs more than the NPU saves.
ON THIS SHARED-MEMORY DESIGN
All three processors address one pool of memory.
Handing work over means agreeing where it is.
Nothing moves, so the handoff is effectively free.
The catch we designed around
Shared memory does not mean every processor can reach every buffer automatically. Access is granted by how memory is allocated, so we verify provenance rather than trusting that a read happens to work.
Hybrid NPU + GPU Execution · MorphiZen HIP EP
4

## Slide 5
THE CONSTRAINT
One non-negotiable requirement
No data is copied when execution moves between the NPU and the GPU.
Why it is a requirement and not a goal: the shared data is the largest item in the system and grows with conversation length. Copying it would erase the benefit entirely.
The failure mode is silence
A copy still produces the correct answer. It only shows up as lost performance, so testing accuracy can never find it.
So it is enforced, not reviewed
Memory is accepted only from approved sources, and every test counts the copies and requires the count to be zero.
And it is a stop condition
If no approach achieves it, we escalate and revisit the architecture rather than ship a version that copies.
Hybrid NPU + GPU Execution · MorphiZen HIP EP
5

## Slide 6
IMPLEMENTATION
What we are building
Six additions. The existing GPU compiler and runtime are extended, not replaced.
Compatibility layer
A thin boundary to the NPU software stack, isolating its dependencies from ours.
Substitute for testing
A stand-in for the NPU so most work is verified without hardware.
Shared memory pool
Working space the NPU can reach, alongside the memory we already manage.
Provenance registry
Records where every buffer came from, so an invalid one is rejected outright.
Compiler output
Turns a claimed model into a sequence of NPU operations, or declines it.
Runtime executor
Carries out that sequence, and falls back safely to the GPU at any point.
Deliberate choice: most of this is verifiable on an ordinary developer machine. Only correctness and performance need the NPU.
Hybrid NPU + GPU Execution · MorphiZen HIP EP
6

## Slide 7
SEQUENCING
Delivery plan
Nine stages. Every stage carries at least one formal checkpoint that must be signed off before the next begins.
0
Prove the risky assumptions
2 checkpoints
1
Boundary to the NPU stack
1 checkpoint
2
Shared memory and enforcement
2 checkpoints
3
Compiler produces a plan
1 checkpoint
4
Routing and execution
2 checkpoints
5
Operation coverage
1 checkpoint
6
Handling unsupported operations
1 checkpoint
7
Loading model weights
1 checkpoint
8
Full end-to-end generation
1 checkpoint
39
tasks in total
12
checkpoints, any of which can halt the project
20
of those tasks need the NPU machine to sign off
Hybrid NPU + GPU Execution · MorphiZen HIP EP
7

## Slide 8
STATUS
Where we are today
COMPLETE
Design and task breakdown
Reviewed. Memory layouts confirmed compatible, which retired the largest technical risk.
AWAITING HARDWARE
Two Phase 0 checks
Software is written and reviewed. Both need the NPU machine to run, which is a scheduled trip.
BLOCKED
Everything after Phase 0
Held deliberately. The memory question decides the architecture, so we do not build ahead of it.
The one thing that would change the plan
Zero copy depends on the NPU being able to use memory our software allocated. That has never been tested in this combination. It is the first thing we check, on purpose — a negative result is an architecture decision, not a delay, and we would rather find it now than in Phase 5.
Hybrid NPU + GPU Execution · MorphiZen HIP EP
8

## Slide 9
RISK
Risks, and how we find out early
Three findings would invalidate the approach rather than complicate it. All three are checked before the bulk of the work.
Shared memory cannot be shared
The NPU rejects memory our software allocated, so a copy would be unavoidable.
Checked in Phase 0
The software stacks conflict
Our runtime and the NPU's cannot coexist in one process. We have been bitten by this class of problem before.
Checked in Phase 0
Too much falls back to the GPU
If the NPU cannot handle enough of the model, the arrangement loses its benefit.
Detected automatically at build time
Each checkpoint states who can sign it off. Work that needs the NPU cannot be closed by a successful run on a developer machine.
Hybrid NPU + GPU Execution · MorphiZen HIP EP
9

## Slide 10
DEFINITION OF DONE
What success looks like
Both models run split across NPU and GPU
Llama-3.2-1B and Llama-3.1-8B, in one session, through one execution provider.
Nothing is copied, and we can prove it
Copy counters read zero across a full generation, with no debug path active.
Answers match a trusted reference
Output matches a CPU reference run; quality measured within tolerance.
Today's performance is not regressed
Word-generation speed and accuracy are unchanged from the current GPU-only path.
Accuracy is the acceptance criterion
No stage is signed off on a speed number. Performance work follows once the arrangement is correct — which keeps us from optimising something that is subtly wrong.
Hybrid NPU + GPU Execution · MorphiZen HIP EP
10